## Slide 1: Astronomical Seeing The Astro-Imaging Channel Dr. Gaston Baudat Innovations Foresight, LLC

## Slide 2: Seeing
Astronomical seeing is the blurring of astronomical objects caused by Earth's atmosphere turbulence and related optical refractive index variations (air density fluctuations).
It impacts the intensity (scintillation) and the shape (phase) of the incoming wave front.
This presentation will ignore scintillation.

## Slide 3: Wavefront and phase distortion
An incoming plane wave is perturbed by the Earth atmosphere turbulent structure leading to phase errors.

## Slide 4: Fluid dynamics
The Reynolds’s (O. Reynolds 1883) number Re predicts flow patterns.
For air flow with velocity of few km/h and for length scales of 0.1km to 1km Re > 106.
Therefore the atmosphere is almost always turbulent.
Density
Velocity
Characteristic length
Viscosity

## Slide 5: Source of optical turbulence
Energy is transferred by a turbulence cascade form the outer scale L0 to the inner scale l0 until heat dissipation (friction).
Eddies exhibit different air density -> different refraction index

## Slide 6: Phase structure function
The Kolmogorov’s turbulence model (A. Kolmogorov 1941) assumes an infinite outer scale turbulence (OST) value L0.
The related wave front phase error variance, known as the phase structure function, is given by:
is known as the Fried’s parameter,
or coherence length leading to
a error of ~ 1 radian, or ~l/6. (David Fried 1960)
Some r
(25l)
(-15l)

## Slide 7: The Fried’s parameter
The Fried’s parameter is the diameter for which the rms wave front phase error is about 1 radian, or ~l/6. It is the “average” turbulence cell size.
z zenith angle, the wavelength and
is the atmospheric turbulence
strength at the altitude h.
is a function of the wavelength and increases as .

## Slide 8: Atmospheric turbulence strength
is the profile of the atmospheric strength as function of the altitude h.

## Slide 9: Seeing versus diffraction limit
is the equivalent diameter of a seeing limited scope of aperture D>>
FWHM [“] | 1 | 1.5 | 2 | 2.5 | 3
[mm/inch] | 110 / 4.3 | 74 / 2.9 | 56 / 2.2 | 44 / 1.7 | 37 / 1.5
FWHM [“] | 1 | 1.5 | 2 | 2.5 | 3
 | 110 / 4.3 | 74 / 2.9 | 56 / 2.2 | 44 / 1.7 | 37 / 1.5
Seeing limited
Diffraction limited

## Slide 10: statistics
histogram and seasonal variations for Lick Observatory (CA USA).

## Slide 11: Coherence time
corresponds to the time for which the changes in the turbulence becomes significant (1 radian rms, ~).
One assumes that the turbulence pattern is moved by the wind faster than it evolves:
where is the average wind speed
Typical ~10m/s (~20mph)
is a function of the wavelength and increases as .
Credit Tokovinin

## Slide 12: Statisitics
histogram & cumulative distribution for Xinglong observatory (China).
[mm] @ 550nm | [ms] V = 10m/s (~20mph)
30 | 0.93
50 | 1.5
70 | 2.2
100 | 3.1
300 | 9.3
30 | 0.93
50 | 1.5
70 | 2.2
100 | 3.1
300 | 9.3

## Slide 13: Short term seeing t <<
For exposure times t<< the seeing is “frozen”.
Nb. of speckle
Nb. of AO degree of freedom
decreases as
Diffraction limited operation is easier at longer wavelengths

## Slide 14: Aberrations and seeing
Atmospheric energy transfer goes from the largest (L0) down to smaller scales (l0), the strongest distortions are on the lowest-order Zernike’s modes (~tilt/tip, piston ignored).
(Noll, 1976) decreases as
Zernike’s polynomials
Type of aberration removed (inclusive) | Residual rms phase error [ %]
Tilt/tip | 36%
Defocus | 33%
Astigmatism | 25%
Coma (3rd order) | 23%
Spherical (4th order) | 21%
Trefoild (3rd order) | 19%
Type of aberration removed (inclusive) | 
Tilt/tip | 36%
Defocus | 33%
Astigmatism | 25%
Coma (3rd order) | 23%
Spherical (4th order) | 21%
Trefoild (3rd order) | 19%

## Slide 15: Long term seeing t >>
For exposure times t >> the seeing is averaged.
Tilt/tip removed

## Slide 16: Isoplanatic patch
The angle for which the wavefront error remains almost the same (~l/6) is known as the isoplanatic angle:
~ 5km, is usually few
arc-second across in the
visible band
increases as

## Slide 17: Effect of the isoplanatic angle on AO
AO operation is usually only effective in a very narrow FOV.
Credit R. Dekany, Caltec
Palomar AO system
IR bands: 1200nm, 1600nm, and 2200nm
Guide star offset [“] | FWHM [“]
0 | 0.2
5.5 | 0.3
13 | 0.45 - 0.59
23 | 0.51 - 0.68

## Slide 18: Temporal behavior of seeing
Temporal phase fluctuations derive from spatial fluctuations under the “frozen turbulence” model. Turbulent cells cross the scope aperture D faster than they evolve.
For an exposure time t >
the asymptotic residual rms
phase error is given by:
Where the cut-off time
is given by:

## Slide 19: Residual tilt/tip and centroid error
The “centroid” standard deviation (tilt/tip) for an exposure time t can be approximated by:
Example: D=279mm (11”) =50mm (FWHM=2.3”) =28ms (=1.5ms)
=0.51” =0.09”

## Slide 20: Lucky imaging and seeing
Some time a short exposure image can be close to the diffraction limit. The probability P for a rms phase error at, or below, ~l/6 (one radian) is (Fried 1977):
>3.5, t<<, inside isoplanatic patch
Example:
D=279mm (11”)
=50mm @550nm
0.04 (~1/25 frame)
=84mm @850nm
>0.7 (~18/25 frame)

## Slide 21: Lucky imaging and PSF shape
Set of 10 short exposure frames (tilt/tip removed):

## Slide 22: Seeing and wavelength
The seeing is wavelength dependent. It is worse at shorter wavelengths and better at longer wavelengths.
coherence length (Fried)
coherence time
isoplanatic angle (patch)
~ wave front phase variance
Full Width at Half Maximum
DL performance threshold
Lucky imaging rate of success

## Slide 23: Limitations of the standard Kolmgorov’s model
The Kolmogorov’s model is only valid for and .
When (OST) is finite the seeing exhibits a significant departure from the model, even for small apertures D.
When the lower level turbulence dominates is small, around 10m, possibly down to about 1m.
The effect is the greatest for the first two (tilt/tip) Zernike terms.
A stronger dependence of the FWHM on l compared to the standard Kolmogorov’s model is quite noticeable.

## Slide 24: The Von Karman’s (VK) model
The Von Karman’s (VK) model explicitly accounts for a finite OST value (Theodore Van Karman, 1948).
Worldwide extensive measurements correlate with VK model.

## Slide 25: FWHM and the VK’s model
The VK model depends on a new parameter

## Slide 26: Finite OST and guide star wander
Finite OST values improve the guide star PSF (less tilt/tip).
Longer wavelengths benefice the most.
Better PSF shape higher lucky imaging rate of success.

## Slide 27: Auto-guiding
The goal of auto-guiding is to correct for setup tracking errors.
Those errors are independent of the seeing effect and are fully correlated across the FOV (unlike seeing).
Long term errors: PE, King’ rate, flexure, model, polar alignment, …, require a slow correction rate (10s to minutes).
Short term errors: Mount mechanics (gear box), wind burst, vibrations, …, require a faster correction rate (few seconds).
Short term corrections may be prone to seeing effects.

## Slide 28: Auto-guiding and seeing
The tracking error target is a function of the seeing.
Rule of thumb: RMS tracking error < 1/4 FWHMseeing
The total rms guiding error before any correction for a given exposure time is given by:
Seeing | Excellent 0.5” | Good 1.0” | Average 2.0 ” | Bad 3.0”
rms error | 0.13” | 0.25” | 0.50” | 0.75”

## Slide 29: Auto-guiding/AO rates
Let’s assume cancels indeed the tracking setup errors.
Total error after correction inside the isoplanatic patch:
seeing limited image, ~diffraction limited image if
Total error after correction outside the isoplanatic patch:
seeing limited image, ~1.4 x seeing limited image!
K decreases when , and at longer wavelengths. The standard deviation decreases (and so K) asymptotically as . However seeing is a stochastic process and should be chosen with enough safety margin.

## Slide 30: NIR versus visible auto-guiding
M83 with full spectrum guiding (OAG)
30
(c) Innovations Foresight 2013 - Dr. Gaston Baudat
M83 with NIR guiding (ONAG)
Mario Motta’s relay telescope 32” (0.8m) @ f/6
M86 images with STL11000 + AO-L (few Hz)

## Slide 31: Thank you!
Clear skies!
Innovations Foresight, LLC
A s t r o n o m y